### Block Exercise

Prerequisite                Navigating the interface, file management, opening and saving of file.

Knowledge

Focus of the Lesson    On completion of this exercise you will have used:

- Sketch line

- Automatic relations

- Smart dimension

- Extruded Boss/Base

- Renaming a Feature

- Editing a Sketch

Commands Used	Line, Extruded Boss/Base and Edit Sketch.

Getting Started

New Part		Click File, New on the standard

toolbar. Select Part from the

New Solidworks Document

dialog box. Select OK.

Saving the Part		Select File, Save as on the standard

toolbar. Save the part in your chosen

location as Block. A part is identified

by its extension *.sldprt . It is

recognised as good practice that a

new folder would be used for each

project created.

Continue to save periodically

throughout the exercise

Command Manager     To activate the command manager

Where to start?		The only feature of the part to be created is the Block. This will be 				an extruded feature based on a sketch.

Sketch to generate the feature

Getting started

Choosing a plane	Select Top Plane from the manager tree.

When you select the top plane four options

will appear over the Top Plane. Select the

sketch icon        from this list of options.

To view the sketch toolbar press S on you

Keyboard.

Creating a sketch	Click the Line           command and sketch a

horizontal line coincident with the origin.

Coincident Relation	The origin is an endpoint to the line and therefore there is coincident

relation between the endpoint and origin.

The “   ” symbol appears at the cursor, indicating that a Horizontal relation is automatically added to the line.  Click again to select the endpoint of the line

Draw a line ensuring that a vertical     relation is automatically added.

Inferencing		Drag a Horizontal line and using Inferencing

choose its endpoint directly over the origin.

Inferencing lines are dotted lines that appear

as you sketch. When your pointer approaches

highlighted cues such as midpoints, the

inferencing lines guide you relative to

existing sketch entities.

Finish the shape by drawing a vertical line and select the origin as the end point as shown.

Turning off tools	Turn off the active tool using:

Press the Esc key on the keyboard

To view the sketch toolbar again press S on the keyboard.

Dimensioning the          Select Smart Dimension          from the sketch toolbar to dimension the 	sketch			sketch.

Using        select the line shown.

Click a second time to place the text of

the dimension to the left of the line.

The dimension appears with a Modify

tool displaying the current length of the

line.

Set the value                 Change the value to 100 and click Save

option.  The dimension forces the length of the

line to be 100 mm.

Pressing Enter has the same effect as clicking

the Save       button

Add additional linear dimensions to the sketch as shown

Zoom to Fit	When dimensioning the sketch may become too large in the work area.  To overcome this press F on the keyboard and the sketch will automatically fit in the work area

Note – The sketch changes from blue to black when it is fully defined.

Exiting the Sketch	To exit the sketch, select the sketch tool on the

confirmation corner, sketch will be saved. Selecting

X will discard changes made.

Creating the feature     Having exited the sketch, press S on the keyboard

to view the features toolbar.

select Extrude Boss/ base from the toolbar.

By choosing Extruded Boss/Base        , the sketch rotates to a trimetric view with a preview of the proposed extrude.

Extrude Feature Settings

End Condition = Blind

Blind End Condition	Extends the feature from the sketch plane for

a specified distance.

Depth = 215mm

Click OK button        to create the feature.

Alternatively select the           from the

confirmation corner

Completed feature	This is the first completed feature of the

part. The sketch has been absorbed into

the EXTRUDE 1 feature in the Feature

Manager.

Renaming a feature	Select the feature in the Feature Manager

Tree. Press F2.

The feature name will be

highlighted with a flashing cursor on

the right hand side. Type the new name to

replace it.

Editing Sketch		On the FeatureManager design tree select the

plus beside the Block feature so that Sketch1

appears.

Right click on Sketch1 and select the Edit Sketch icon.

The original sketch used to create the feature

appears, with the feature shown as an orange preview.

Editing Dimensions	Double click on the 100mm dimension.  The Modify

Tool  appears displaying the current length of the

line.

Change the value to 215 and click Save

option.  The dimension forces the length of the

line to be 215 mm.

Note you may also change any of the dimensions of the

Block by selecting any face of the block and dragging

the blue dot at the end of the chosen dimension.

This activates the ruler, you can set the desired

Dimension by scrolling along this ruler. If you

Scroll the cursor on the ruler it will move in 5mm

Increments, but if you scroll with the cursor to the

Side of the ruler it will move in .1mm.

Exiting the Sketch 	To exit the sketch, select the sketch tool on

the confirmation corner.

Save and close		Click Save          to save your work and click File, Close to close the part.