### Calculator Exercise

Commands Used		This lesson includes Sketching (including Text), Extruded Boss/Base, Extruded 				Cut, Fillet, Chamfer and Linear Pattern.

Getting Started		Create a sketch, on the front plane using the dimensions shown. Position the 				sketch 	such that the origin is in the lower right hand corner.

Extruded Boss/Base	Extrude the sketch using the

Blind End Condition and a

Depth of 75mm

Extruded Cut		Sketch the rectangle on the sloping

surface and Smart Dimension

as shown.

Extrude Cut the sketched rectangle

to a depth of 2.5mm.

Adding the buttons	Create a rectangular sketch

on the top face.

Smart Dimension

as shown.

Create a Sketch Fillet

on the corners of R4mm

and R1.5mm.

Extrude the sketch to a

Depth of 1mm.

Create a Fillet of 0.15mm

on the top edge of the button.

Linear Patterning	Create a Linear Pattern using the settings shown.

The fillet must be selected

independently of the button

feature, in features to

pattern, to create the linear

pattern

Function Buttons		Create the sketch of the function buttons using the sketch dimensions below.

Extrude Boss/Base	Extrude the sketch to a

Depth of 1mm

Fillet			Add a Fillet of 0.2mm

to the top face of the

feature

Linear Patterning	Create a Linear Pattern using the settings shown.

Creating the ‘=’ 		Create the sketch as shown.

Button

Add a Collinear Relation

between the lines and the existing

features to fully define

the sketch.

Extrude the sketch to a Depth of

1mm .

Add a Fillet of 0.2mm as before.

Main Body Fillet		Add a 3mm fillet to the edges shown below. Note the omitted edges.

Add a 20mm fillet to the remaining two edges at the intersection of	 the

top faces.

Screen Chamfer		Create a 1.5mm x 45º Chamfer

to the screen edge as shown.

Text			Add Text to the lower

buttons as shown.

Cut Extrude the sketch

to a depth of 0.2mm

Add the Text to the upper

buttons as before.

Cut Extrude the sketch

to a depth of 0.2mm

Create a sketch on the sloping

face and add the text shown.

Extrude Cut the text to a depth

of 0.1mm

Completed Model

Edit Colours and		Edit the colour and texture settings to make the model look more

Textures			realistic, as shown on the front page of the document.

Lesson Complete!