### Digital Camera Exercise

Commands Used		This lesson includes Sketching, Extruded Boss/Base, Extruded Cut, 					Fillet, Chamfer and Text.

New Part			Click File, New on the standard toolbar. Select Part from the New 						SolidWorks Document dialog box. Select OK.

Saving the Part		Select File, Save as on the standard toolbar. Save the part in your chosen 					location as camera. A part is identified by its extension *.sldprt . It is 					recognised as good practice that a new folder would be used for each 					project created. Continue to save periodically throughout the exercise

Where to start?		The first feature of the part to be created is the body of the camera. This will be 				an extruded feature based on a sketch.

Sketch to generate the feature

Extruded Feature

Getting started

Select the top plane from the feature manager the sketch command will appear. The selected plane will rotate to a normal to view and the origin will be displayed.

Creating a sketch		Using the Rectangle   command, create a sketch, from the origin as shown, 				approximately 100mm x 25mm. Ensure that all lines are either horizontal or 				vertical indicated by the relations.

Select the Circle    command from the sketch toolbar. Choose a point 				coincident       with the back line as the centre and drag as shown below, click to 				form the circle.

Using the Trim Entities  command, select the areas of the circle and the 				front edge to be removed.

Dimensioning the		Select Smart Dimension               from the sketch toolbar and dimension

sketch                               	sketch as shown below.

Note – The sketch changes from blue to black when it is fully defined.

To exit the sketch, select the sketch tool on the 					confirmation corner, sketch will be saved. Selecting

X will discard changes made.

Creating the feature	Select Features from the Command Manager. The Features toolbar has now 				replaced the Sketch toolbar along the top of the screen

Choose Extruded Boss/Base, the sketch rotates to a trimetric view with a 					preview of the proposed extrude.

Extrude Feature Settings

End Condition = Blind

Depth = 62mm

Click OK button  to create the feature.

Alternatively select the       from the

confirmation corner

Completed feature	This is the first completed feature of the

part. The sketch has been absorbed into

the EXTRUDE 1 feature in the Feature

Manager.

Renaming a feature	Select the feature in the Feature Manager

Tree. Press F2.

The feature name will be

highlighted with a flashing cursor on

the right hand side. Type the new name to

replace it. (Camera Body)

Adding the camera lens

Sketching on a face	Select Sketch on the Command Manager. Sketch toolbar replaces the feature 				toolbar at the top of the screen.

Select the front face of the camera and select sketch.

Select Normal to from the Heads Up Toolbar

Creating the sketch	Sketch a circle on the face and dimension as shown.

Creating the		Select Features, Extruded Boss/Base. Choose Isometric View                      cylindrical feature	from the Head Up Toolbar

Extrude Feature Settings

End Condition = Blind

Depth = 4mm

Creating concentric	Use the same procedure to create two further concentric cylindrical features

features			as shown below.

To ensure 		When sketching the circle on the face of the existing cylinder move the cursor concentricity of the	over the edge as shown in fig. 1, without clicking, to display the centre of the three cylinders		face. Move the cursor back to the centre, select the centre point and drag the 				radius, as in fig. 2.

Using Extruded Cut	To remove the shutter from the front of

the lens, a sketch is generated on the

face having the desired profile. This is

then cut from the solid to the required

depth using Extruded Cut.

Creating the shutter	Create a sketch on the front face

sketch.			of the lens and choose Normal To view

from the view toolbar. Sketch a rectangle

as shown and add in a diagonal

centre line.

Adding a concentric	To ensure that the shutter remains in the centre, a relation must be created

relation 			between it and the circle.

Right click on the centreline and choose Select

Midpoint. Holding down the control key choose

the circumference of the circle.

On the left hand side choose Concentric

from the Add Relations dialog box shown below.

Select        to close the dialog box. The rectangle

will move to the centre of the circular face.

Adding dimensions	Because the sketch is blue it is not

to fully define a		yet full	defined. Using

sketch.			Smart Dimension define the

sketch as shown opposite.

The sketch now turns black and

is fully defined.

Exit the sketch using the

Confirmation Corner.

Select a 3-dimensional

view from the Heads Up Toolbar

Creating the		From the features toolbar choose

Extruded Cut		Extruded Cut. When prompted

feature.			select the rectangle as the sketch

for extrusion.

The Cut Extrude dialog box appears

on the left with a preview of the

extrusion.

Cut Extrude Feature Settings

End Condition = Blind

Depth = 2mm

Click OK button      to create the feature.

Adding the raised	To create the raised profile on the back of the camera, a rectangular sketch profile on the back	is required, positioned on the back face.

Rotate View		It is necessary to rotate the model to choose the back

face as the surface on which to create the sketch.

Within the graphics area click the Right hand mouse

button and select the rotate  command. Rotate the model

until the back surface is exposed.

Sketching

Create a sketch and choose the back surface as the plane on which to build the 	sketch. Sketch a rectangle on the back face and dimension as shown.

Exit the sketch

Dimensioning		Should the overall size of the camera change the raised panel will remain 					offset 5mm from the altered dimension.

Creating the extruded		Choose Extruded Boss/Base from the features toolbar

panel feature.			Select the rectangle as the sketch to create the feature

Extrude Feature Settings

End Condition = Blind

Depth = 3mm

Rotate to a 3 dimensional

view to ensure the extrude

direction is correct

Click OK button            to

create the feature

Removing the screen		Similar to the shutter, the screen is produced using an Extruded Cut.

The face of the extruded rear panel is used as the sketch plane. Sketch 					dimensions are shown below along with feature settings

Inserting the back		The function buttons will be added as an

function buttons.			Extruded Boss/Base feature

Create a new sketch and choose the face of the

extruded panel as the sketch plane. Select a

Normal To view from the View toolbar.

To ensure that all of the buttons remain vertically aligned, a vertical centre 	line will be added and the centres of the circles will be made coincident 	with it.

Choose Centerline from the sketch

toolbar and add in a centerline as

shown.

The vertical relation symbol

indicates that the line is vertical.

Adding the sketch 		Sketch the four circles as

shown ensuring that each

centre is coincident

with the vertical centreline.

Diameter sizes are irrevelent

at this stage.

Adding an equals			In order to make the three smaller

relation				circles equal radii it is necessary

to add an Equal Relation.

Select Add Relation command and

select the top three  circles

In the Add Relations 	dialog box

select Equal

Adding dimensions		Dimension the sketch

using Smart Dimension.

When the sketch entities

turn black, the sketch is

fully defined.

Exit the sketch

Creating the feature		Extrude the feature using the feature settings below.

Creating the Capture		This button will be created with two concentric extrusions similar to the

Button.				construction of the front lens.

Sketching				Create a sketch using the top surface. Select Normal To view from the 					Heads Up toolbar.

Sketch a centre line with the Sketch

Relations shown.

Sketch a circle with its centre coincident

with the midpoint of the centerline

and Smart Dimension as shown

Fully Defined			The sketch has turned black!

Why is the sketch Fully Defined with

the addition of just one dimension?

Because of the inclusion of the Sketch

Relations

Change Orientation		Choose Trimetric View from the view toolbar

Extrude Boss/Base		Extrude the sketch to a depth of 2mm

Capture Button			To complete the capture button

a further sketch and extrusion will

be required.

Create a sketch on the top face of the

existing cylinder. Sketch a circle of

Ø10mm.

Ensure that the circle is concentric to

the face by selecting the face centre

as before.

Extrude Boss/Base		Extrude the sketch to a

depth of 1mm.

Introducing Text			The Text tool allows you to insert text into a sketch and extrude as a 					boss/base or cut feature.

Construction lines must be added to guide the text

Text Sketch			Create a sketch on the front

face and add the centreline

as shown

Adding text			Select text     from the sketch

toolbar.

Select the centerline as the text guide

Type SAMSUNG into the text window

Use Document Font will be selected by

default. Deselect by clicking on the tick

next to it. Font is no longer greyed out.

Select Font.

Choose Arial Black, Regular, Size 2.5mm

Select OK

Select        to exit the command.

Changing text 			The length and position of the line,

position				and hence the position of the text, may be varied

by holding down the left mouse button on the

endpoint of the line and dragging the line.

Creating the text			Extrude a boss with a

feature				Depth of 1mm.

Introducing Fillet		Fillets are generally added to the solid rather than the sketch and are 					hence referred to as applied features	.

Where to find it			Select the Fillet tool  from the features toolbar

Insert Fillet			Select the Fillet option. The fillet options

appear in the property manager.

Set the Radius value to 2.5mm

Select Full Preview

Edge Selection			The edges will highlight red as the

cursor moves over them and appear

green as they are being selected.

Select the edges shown and click OK

It may be necessary to rotate the solid

to select all edges.

Removing edges 			Should an incorrect edge be chosen,

from selection			right click on the selection name in

the fillet dialog box and choose Delete.

That edge will be removed from the list.

Clear Selections will delete all.

Further fillet 			Create a further 1.5mm fillet to the

edge of the rear panel and the rim of the

capture button as shown.

Introducing Chamfer		Similar to Fillet, Chamfer is an Applied Feature. Chamfer creates a 					bevel on one or more edges. A chamfer may be defined by two distances 					or a distance and an angle.

Where to find it			Select the Chamfer tool    from the features toolbar

Insert Chamfer			Select the Chamfer option. The chamfer options

appear in the Chamfer Property Manager.

Add a Chamfer

using the edge of

the lens as shown.

Set the distances

using the values

shown on the

right

Select OK.

Chamfer distance/angle		Select Chamfer.

Add a Chamfer

using the edge of

the shutter as shown.

Set the options as

shown opposite

Select OK.

Exercise Complete!

# Text boxes

Ø30mm x 7mm

Ø25mm x 10mm

Fig.1 – Using the cursor to determine the face centre

Fig.2 – Move the cursor to the centre, select and drag the radius