### Cavity Block Exercise

Prerequisite		Creating a Part, Saving a Part, Creating a Sketch, Drawing Lines,

Knowledge		Automatic Relations – Vertical, Horizontal, Coincident.  Smart 						Dimensioning, Extruded Boss/Base (Blind End Condition).

Focus of the Lesson	On completion of this exercise you will have used:

- Sketch rectangle

- Centre line

- Equal relations

- Sketch mirror

- Extruded Boss/Base

- Extruded Cut

Commands Used	Rectangle, Centreline, Add Relation, Sketch Mirror, Extruded Boss/Base and Extruded Cut.

Getting Started

New Part			Create a new part.  Save the part as Cavity Block in your chosen location.

Getting started

Where to start?		The first feature is the main part of the block and we will then remove the two 				cavities.

Choosing a plane		Select Top Plane from the manager tree.

When you select the top plane four options

will appear over the Top Plane. Select the

sketch icon         from this list of options.

To view the sketch toolbar press S on you

keyboard.

Creating a sketch		Click the drop down arrow beside the

Rectangle           command, now select the

Centre Rectangle command.

create a sketch of the rectangle using the origin

as centre.

Dimension Sketch         Select Smart Dimension          from the

sketch toolbar to dimension the sketch

Smart dimension the sketch to

The values shown.

Zoom to Fit		Press F to resize the view to fill the screen.

Exit the sketch.

Creating the feature	 Press S on the keyboard and then choose

Extruded Boss/Base        from the Features Toolbar.

Extrude Feature Settings

End Condition = Blind

Depth = 215mm

Click OK button         to create the feature.

Renaming a feature	Select the Extrude feature in the Feature Manager

Tree. Press F2.

Type the new name Block to replace it.

Creating the Cavities

Sketching on a Face	Any face of a model may be used to generate a plane to contain a sketch.

Select	the top face of the block.  Then select the sketch icon      from the

List that appears.

Change View                   From the options on the top of the

graphics area select the View orientation

icon and select Normal To         . This

allows us to look in on the surface at a

90 degree angle.

Create a new Sketch	To create a new sketch select the sketch icon from the

List on the chosen surface.

Then Press S to view the

Sketch toolbar.

From the sketch toolbar

Select centreline from

The line command.

Draw a line from the midpoint of the horizontal lines.

The midpoint is automatically located

when the cursor hovers over the

required line.

Draw a second centreline from the

origin to the midpoint of one of the

vertical lines.

Rectangle Command	Press S and select the Centre Rectangle

Sketch command and draw 2 rectangles

On the centre line.

Press ESC on your keyboard

Dimension sketch 	Dimension the sketch using the dimensions shown.

Exit Sketch.

Isometric View		Select Isometric  from the View Orientation toolbar.

Extruded Cut		Cuts a solid model by extruding a sketched profile in one or two directions.

Press S on the keyboard and select Extrude Cut from the

Features toolbar.

Cut Extrude Feature Settings

End Condition = Through All

Through All		This type of end condition always cuts through the

End Condition		entire model no matter how far.

Depth is ignored because the Extruded Cut is

Through All

Click OK button            to create the feature.

Completed feature

Renaming a feature	Rename it Cavity

Save and close		Click Save  to save your work and click File, Close to close the part.

Exercise Complete!