### Chocolate Bar Exercise

Commands Used		This lesson includes Sketching, Extruded Boss/Base(with draft),

Extruded Cut, Fillet and Linear Pattern.

Getting Started		Create a sketch, on the top plane using the dimensions shown. Position the sketch 				such that the origin is in the lower left hand corner.

Creating the feature	Select Extruded Boss/Base

Choose the Blind option from the list and

enter a Depth of 6.5mm.

Adding draft		Draft will slope the edges of an extruded boss.

Where to find it		Select Draft On/Off,        enter a value of 10º.

Choose OK

Adding the top blocks

Creating the sketch	Create the rectangular sketch

on the top face and dimension

as shown.

A sketch may be defined using

edges and features which are

not on the active sketch plane.

Extrude Boss/Base	Extrude Feature Settings

End Condition = Blind

Depth = 4mm

Draft Angle = 15º

Choose OK

Text

Generating the text	Create a sketch on the top surface of

the chocolate block.

Add a diagonal line as a Centerline.

Draw another line on the surface and

add a Paralell Relation.

Adding Text		Select Tools/Sketch Entities/Text

or select text           from the sketch

toolbar.

Select the parallel centerline as the text guide

Type Cadbury into the text window

Use Document Font will be selected by

default. Deselect by clicking on the tick

next to it. Font is no longer greyed out.

Font Details		Choose Font and make the selections as shown. Select OK

Text Spacing		SolidWorks will not extrude a sketch with

overlapping lines or regions. Script

text utilises such overlapping regions, as

shown opposite. To eliminate these, the

spacing between the letters must be increased.

Increasing spacing	Increase the spacing            to 120% to

eliminate the overlapping regions, as shown

below.

Choose OK

Creating the feature	Extrude Cut the

text to a depth

of 0.2mm

Fillet			Create a fillet of 0.35mm radius on all

of the edges of the top block.

Create a second fillet of 0.35mm on

the edges of the lower block, excluding

the base edges.

Note			These fillets were created individually

because, the edges of fillet1 must be copied to form the

remaining top blocks whereas the edges of fillet2 are not.

If they were formed in one feature it would prove more difficult to

select them.

Patterns			Patterns are used when creating multiple instances of one or more features.

Linear Array		This can be a one or two directional array.

Where to find it		On the features toolbar click the Linear Pattern tool

Select the linear edge of the base

in front as Direction 1, with a

Spacing of 25mm and

Number of Instances = 4

Select the linear edge on the side

as Direction 2, with a Spacing of 22mm

and Number of Instances = 2

To select Features to Pattern click in the

Features to Pattern Window, it turns pink.

Flyout Feature 		Expand the Feature Manager Design Tree by

Manager Design		clicking on the plus ‘+’ sign next to the file name

Tree			on the top left hand side of the Drawing Area.

It expands as shown on the right.

Choose the Chocolate block, extruded text and

the fillet1 features as features to pattern

A preview is displayed in the drawing area.

Reverse Direction	If necessary, select Reverse Direction       next to each Pattern Direction, to set 				the direction shown.

Choose OK

Edit Colour		With the cursor positioned over the file

name at the top of the Feature Manager

Design Tree, right click Select Appearance

Choose an appropriate colour from the colour swatch. Select OK

Lesson Complete!