### Desk Tidy Exercise

Object Analysis sheet

New Commands used:

Getting started:

Create Sketch			Select the Top plane to sketch on.

Create the sketch shown on the Top plane.

Add Relation			Add an Equal Relation to two edges of the rectangle.

Smart Dimension		Apply dimensions to the sketch using only the dimension displayed.

Full define the sketch.

Create Extrude 		Select Extruded Boss/Base from the Features menu.		.

Add Depth and End 		Ensure that the End condition is Blind and the Depth is 100mm.

condition

Create Sketch			Select the Top surface of the cube to sketch on.

Create Sketch	Sketch the diagonals of the face and as shown, change the line properties to                             for construction as shown.

Create Sketch 	Sketch the shapes as shown, fully define the sketches

Create Extrude 	Select Extruded Cut from the Features menu. Ensure that the End condition is Blind and the Depth is 35mm.

Create Fillet 	In the Features menu select Fillet as shown. Select Fillet Expert.

Add Text	Select the front face of the cube. Sketch a line on the face using the measurements as shown. In the Sketch menu select Text as shown and change the Text properties as shown.

Create Extrude Cut of Text 	Select Extruded Cut from the Features menu. Ensure that the End condition is Blind and the Depth is 1.5mm.

Adding an Appearance to the Desk Tidy

Right click on any face of the model and choose

Appearance Callout

A drop-down menu appears with the various aspects of the model in hierarchical order.

Click on the colour swatch next to the part name, Desk Tidy.

The RealView/PhotoWorks Tab appears on the right hand side of the screen

and the Colors Appearance manager on the left as shown overleaf.

A preview window appears to preview the resulting render.

Within the RealView/PhotoWorks tab we can access appearances, scenes, decals and lights folders.

Choose Appearances. The categories are listed on top with the various options within each category displayed below.

Choose Organic, Miscellaneous, Sponge.

The Sponge effect is applied to the entire part.

Choose OK

Other Possible Extrude Options