### Introduction to Loft -  Hyperboloid of Revolution Part (B)

Prerequisite Knowledge	Previous knowledge of the following commands is required to complete this lesson, sketching (line construction, circle, add relations, dimensioning, convert entities), Inserting Planes, Loft Boss/Base, Cut with surface.

Focus of the Lesson	Loft creates a solid feature by making transitions between profiles.

On completion of this lesson you will have the used the following aspects:

- Inserted reference planes to create the model.

- Created a Hyperboloid of Revolution (double ruled surface) using the Lofted feature.

- Surface cut to locate the Asymptotes of the Hyperboloid of Revolution.

- Covert entities to locate the Directrix and locate the Focus of the Hyperbola.

Commands Used	This lesson includes Sketching (line, circle, Smart Dimension, covert entities), Inserting Planes, Loft Boss / Base, Cut with surface and Appearance.

Where to start?		How is a Hyperboloid of Revolution created?

There are numerous ways in which a Hyperboloid of Revolution can be

modelled in SolidWorks.  Here are a few of the methods which can be used:

- Revolve a Hyperbola about an axis.

- Loft a circle along one of the straight line

elements.

Note: The straight line element could also be revolved

about a central axis. But SolidWorks will not allow

an open sketch to be revolved.

3. Sweep a circle along a Hyperbola guide curve.

Note: For the purpose of this exercise the focus will be the lofted method.

Getting started		What sketches are required to

create a lofted Hyperboloid of Revolution?

The following sketches are required:

- Base Circle

- Top Circle

- Straight Line Element

Note: A sketch plane is required for each of

these sketches.

Sketch the base		Create a sketch of the base circle on

the Top Plane as shown.

Note: The circle is constructed with it

center on the origin.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Base Circle”

Save part			Save        part as Hyperboloid of revolution.

Insert sketch planes		Select Reference Geometry and Plane on the

features toolbar.

OR

Select Insert, Reference Geometry and

Plane.

Plane parameters	Choose the top plane as the reference entity and

set the distance as 80mm.

Set the number of planes to create           to 2 planes.

Note: Only one of these planes is required to model the Hyperboloid

of Revolution. The middle plane is being setup to locate the throat circle

later in the exercise.

Click OK button              to create the plane

Rename Plane		Rename the planes as shown.

Sketch the top		Create a sketch of the Top circle on

the Top of loft Plane as shown

Note: The center of the circle is

collinear with the origin.

Insert plane for		Select Reference Geometry and Plane       .

straight line element		Choose the front plane as the reference entity and

set the distance as 30mm.

Click OK button              to create the plane.

Rename plane		Rename the plane “element plane”

Sketch straight line		Create a sketch on element plane.

element

Construct a centerline and one

straight line element between the

base and top circles as shown.

Note: The straight line element must now

be constrained to the circles to construct

the surface.

Constrain the element	The straight line element must be fixed centrally between the circles.

Right click on the straight line element and choose

Select Midpoint. Holding down the control key

choose the centerline.

On the left hand side choose Coincident

from the Add Relations properties.

Note: As there are so many sketch planes currently active. Hide some of

the sketch planes to get a clear view of model.

Add Relations between	Add relation to endpoint of the element and

sketches			the top circle.

Select Add relations                from sketch toolbar.

Select the endpoint and top circle. Choose Pierce

from the add relations window.

Note: The two sketches are now intersecting each other.

Add Pierce relation to the endpoint of the element

and the base circle as shown.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Straight line element”

Lofted Boss/Base		Select the base circle and top circle as the

profiles.

Guide Curves Selection	Select Single Contour Select           to select the guide curves.

Select the Guide Curves window and choose straight line element as shown.

Click OK button           to create the Hyperboloid of Revolution.

Locate Asymptotes		Create a vertical cut through the Hyperboloid of Revolution to find the

Asymptotes of the Hyperbola.

Where can this vertical section taken?

A vertical section can be taken in any position

about the Hyperboloid of Revolution once it is taken tangential to

the throat circle as shown to locate the Asymptotes.

Note: In this case a vertical section plane parallel to the front plane will

yield the best view. Therefore having already setup a plane in this position

element plane, this can be used.

Create vertical		Select the Element plane in the

section plane			FeatureManager.

Cut with surface		Choose Cut with Surface,                  from the features toolbar.

OR

From the top toolbar, select insert,

cut, with surface.

SurfaceCut			The featureManager will appear with

the element plane selected as the surface cut

as shown.

The direction of the cut can be selected

using the flip cut           option.

The arrow in the middle of the part indicates

which side of the part is going to be removed

when cut.

Click OK button        to create the surface cut.

Note: The two straight line elements located are used to created the double

ruled surface (Asymptotes).

Locate the Hyperbola’s	Select front plane in the featuremanager and sketch

Rotate the Hyperboloid of Revolution

into a perpendicular view

as shown.

Note: The Double Hyperbola can now be seen

along the edge of the Hyperboloid of

Revolution.

Locate Hyperbola		Select one of the Hyperbola’s as shown.

Select Convert Entities             from the

sketch toolbar.

OR

Select Tools, Sketch Tools and Convert

Entities.

This has now created a sketch of the Hyperbola

on the front plane as shown.

Repeat the procedure for the Hyperbola on the

opposite side.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Hyperbolas”

Locate throat circle		The throat circle is located tangential to the vertical section and passes

through the vertices of the Hyperbola’s. Having a plane already setup

in this position the Throat Plane, the circle can be created on this plane.

Select the Throat plane and sketch

Create the circle as shown tangential to the

vertical section.

Note: Select normal to		 to see the

plane as an edge view.

Add Relation			Add a tangent relation                        between

the circle and vertical section fix circle to

correct position.

Analyse the geometry	On which plane would the geometry of the Hyperboloid of Revolution be

constructed to get the best results/view.  In this case the front plane or element

plane (vertical section) would be the most suitable. As each have some of the

necessary geometry (Asymptotes and Hyperbola curves). In this case the

element plane will be the most suitable, as the details can be clearly seen.

Show plane			Show the element plane.

Select the plane in Featuremanager and

right click. Select Show to display the plane

in the graphics window at all times.

Locate Hyperbola’s		Create a sketch on the element plane for

the Hyperbola’s.

Note: The double Hyperbola’s have been

located already on the front plane son they can

converted to the element plane.

Select one of the Hyperbola’s on the front plane

as shown.

Select Convert Entities                 from the sketch

toolbar.

The Hyperbola has now be converted onto the

element plane as shown. Repeat procedure for other

hyperbola.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Hyperbolas on element plane”

Locate Hyperbola		Create a sketch on the element plane again

asymptotes			for the Hyperbola’s properties.

Use convert entities to locate Asymptotes

lines as shown.

Note: We have now created two sketches on

the element plane therefore these sketches can

be coloured separately

Locate Auxiliary Circle	Construct a circle            using intersection

of asymptotes as center and drawn up to

hyperbola.

Add tangent relation

between circle and hyperbola.

Draw axis			Construct axis using centerline as shown.

Locate directrix		Construct directrix using line command.

The directrix is located through the

intersection of the auxiliary circle and

asymptotes vertically.

Moving the mouse over the point of

intersection until the intersection symbol

appears. Select and draw directrix.

Note: The directrix line could be drawn vertically and relations added.

But SolidWorks does not allow the selection of the intersection point within the

add relation command.

Draw directrix		Draw directrix lines as shown.

Locate focus points		Construct a line perpendicular from the

asymptote to the axis as shown to find

the focus.

Add relations			Add a perpendicular

relation between the asymptote and line.

Add a merge                     relation

between endpoint of line and

intersection of asymptote and directrix

as shown. To find focus on axis.

Label details			Select Insert, Annotations and Note.

Label the details of the Hyperbola

construct as shown.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “construction details”

Add appearance to		Right hand click on the feature Hyperboloid of Revolution select

Hyperboloid of		Appearance and Color

Revolution

Choose an appropriate colour from

the colour swatch.

Add appearance to		Add appropriate colour to vertical section

vertical section		as shown.

Add appearance to 		Right hand click on the sketch

sketches 			Hyperboloids on element plane select

Appearance and Color

Choose appropriate colour.

Repeat the procedure for the construction detail sketch.

Lesson Complete!

Other Possible Loft Options

Johnson’s Baby Shampoo				      Aftershave Bottle

Hyperboloid of Revolution with door		Hyperboloid of Revolution – circular array

Hyperboloid of Revolution 1998		           	       Hyperboloid of Revolution 2004

# Text boxes

Fully defined sketch of Hyperbola

Hyperbola’s

Cut in this direction

Vertical Section

Throat Circle

Vertical Section Plane

Pierce the element through the base circle

Midpoint of the element is fixed onto the centerline.

Preview of Planes

Number of planes to create

Vertical Section

Asymptotes

Point of intersection

Focus

Origin