### Introduction to Revolved Cut -  A Table Lamp

Prerequisite Knowledge	Previous knowledge of the following commands are required to complete this lesson, sketching (line construction, arc construction, dimensioning), Fillet, Extruded Boss/Base, Extruded Cut, Revolved Boss/Bass, Textures.

Focus of the Lesson	Revolved cut involves removing material by revolving one or more profiles around a centerline.

On completion of this lesson you will have the used the following:

- Selected the correct planes of reference in modelling the part.

- Revolved a sketch contour about an axis to create a revolved cut.

- Revolved a sketch contour about an axis to create a revolve boss/base.

- Revolved a sketch contour about an axis to create a thin revolve.

- Applied textures to the part modeled.

Commands Used	This lesson includes Sketching (Centerline, line, Centerpoint Arc, 3 Point Arc, Smart Dimension), Extrude Boss/Bass, Revolved Cut, Revolved Boss/Base, Fillet, Extruded Cut, Revolved Thin feature and Textures.

Where to start?

Note: This table lamp would normally be modeled as

an assembly. But has been modeled in this exercise as

a part to demonstrate the following applications:

- Revolved Cut  -  Lamp Stem

- Thin Revolve  -  Lamp Shade

We will start with a square section of material for the stem just as if the lamp was being manufactured using a wood lathe.

Selecting a Plane		The base of the lamp will sit on the Top

Plane with its centre on the Origin. The 				Front Plane and Right Plane will therefore 				pass through the axis of the stem.

Getting Started		In order for this to happen the sketch for the stem will be created 			on the Front Plane.  It can then be extruded using Mid-plane as 			the end condition.

Open new Part file and save as ‘Table Lamp’.

Select Sketch              on the Features Command Manager.

Select Sketch              from the toolbar and select the Front Plane.

Sketch a rectangle              as shown.

Note: The bottom of the rectangle is drawn above the

origin (approx 20mm).

Adding Relations		To ensure that the rectangle is centered over the 					origin a relation must be first created between the 					two.

Right click on the bottom line of the rectangle

and choose Select Midpoint. Hold down the Control

Key (Ctrl) select the origin.

The Add Relation Property Manager opens.

Select Vertical                      in this property manager

and confirm.

The midpoint of the horizontal side of the rectangle is now located vertically over the Origin.

Dimension the sketch	Dimension the sketch as shown

Note: The sketch is now fully defined.

Confirm the sketch.

Creating the feature		Select Extruded Boss/Bass from the Features toolbar.

Choose the Mid Plane as the end condition and

enter a Depth of 50mm.

Choose            to confirm feature.

Rename Feature		Rename this feature as ‘Stem’

Sketch for Profile		Having the block of wood, you now want to cut (revolve) the profile around

the stem.

The sketch will be created on the Front Plane in this case.

(It could also be created on the Right Plane because the axis is located on both planes)

Select the Front Plane and choose Sketch from the toolbar.

Select Normal To from the View Toolbar to get

a perpendicular view.

Note:	Having a perpendicular view makes it easier

to create a accurate sketch.

Centrelines			Select centerline             and create a central axis

from the mid-points of the rectangle as shown.

Create two centerlines vertically on

the rectangle as shown.

Smart dimension           the centerlines as shown.

Note: When defining a sketch, it is best practice to sketch, add relations, and finally add dimensions.  However, because of the complexity of this sketch the dimensions are indicated as the sketch develops to aid clarity.

Create profile			Select Line             and create the sketch as

shown.

Note: The 450 line is drawn to the first centerline

as shown.

Create circular		Zoom into the bottom area of the sketch.

beads

Select Centerpoint Arc             and construct								four semi circles along the centerline as shown.

Add Relations		Select Add Relations             and select the 4

semi-circles.

Choose Equal        from the Add Relations

dialog box.

Dimensions			Dimension the semi circles, radius 4mm.

Construct line		Construct a vertical Line along the

centerline as shown.

Create top of lamp		Zoom into the top area of the lamp.

Create the sketch using Line command

up to the centerlines as shown.

Note: The perpendicular relation between

the two lines is created automatically using

the inference line as shown.

Dimension Sketch		Using the Centerpoint Arc command create

the semi-circle. Smart Dimension the

sketch as shown.

Complete Sketch		Select 3 Point Arc           from the sketch toolbar.

Construct a 3 Point Arc by choosing the end

points of the 2 beads and select any mid point

for the arc as shown over.

Smart Dimension the Arc radius 1000mm.

Creating the feature		Choose Revolved Cut              from the features toolbar.

OR

From the top toolbar select Insert, Cut

and choose Revolved Cut.

Revolved Cut Feature	The PropertyManager appears

Settings			with these default conditions.

Analyzing the

PropertyManager

Axis of Revolution		         = Axis of Revolution

In this case SolidWorks cannot recognized

which of the centerlines created in the sketch

is the Axis of Revolution. Therefore the axis

is currently empty

Select the correct centerline in the sketch. The

model will now give you a preview of the revolve

cut as shown. Notice the axis of revolution window

now appears like this

Note: Change the model view to isometric or trimetric

to get a better image of the feature.

Revolve Angle		Enter             Angle = 900

The revolved cut preview will alter as shown.

Where the sketch profile will cut rotate through

900.

Revolve Direction		Select           Reverse Direction. The Revolved Cut

will now revolve in the opposite direction as

shown.

Revolve Type			Select Mid-Plane in Revolve Type window as shown.

The sketch profile will now revolve

cut through 900 Mid-Plane within the

block of wood.

Select Two-Direction in the Revolve Type window.

Now you are given the option to enter two angles

The Revolve Cut will now cut in two direction at any

chosen angle as shown.

Selected Contours		Allows you the select a single or number of

individual sketch profiles which are to be

revolved about the axis of revolution.

Enter Required 		Enter              Angle = 3600.

Parameters

Select One-Direction			      in

Revolve Type window

Click OK button        to create the feature.

Rename Feature

Creating the base		Create a sketch on the Front Plane for the base.

Select centerline and construct an Axis of Revolution

from the origin as shown.

Complete Sketch		Select the line command and complete the sketch using the dimensions

shown for the base.

Revolve Boss/Base		Revolve the sketch using the centerline as

axis of revolution and sketch as contour

profiles. Revolve angle of 3600.

Add fillets			Add 3mm fillets to the bottom edges shown.

Create hole for flex		Create a sketch on the top surface of the stem.

Select circle           and construct a circle using the

Origin as centre

Note: Select Normal To                       for a

perpendicular view of top surface.

Dimension circle		Dimension the circle – diameter 8mm.

Extruded Cut			Extrude cut the sketch using the Offset from

Surface end condition.

Select the bottom surface of the base as the Face to offset

from as shown and Depth from surface of 3mm.

Display Style			Select Hidden Line Visible           from the view toolbar.

The view of the lamp will now change as shown.

Note: The position of the hole can be now seen.

Create the hole 		We need to create a hole in the base for the flex.

through the base		The vertical face of the base is circular. We cannot 					create a sketch on this surface.

The lamp has been created with the planes

of reference through the axis of the stem. Therefore the Right Plane or the Front Plane can be selected

to create the circular cut through the base.

The sketch will be created on the Right Plane.

Construct Circle		Create a sketch, on the Right Plane using the dimensions shown.

A centerline is first constructed from Origin for the centre of the circle.

Extruded Cut			Extrude Cut the sketch using the

Through All end condition to

Create the hole.

Lamp is now complete

Lets look at how to model the lamp Shade

The Lamp Shade

Note: This exercise could also be modeled as an assembly.

How to create the		The lamp shade is a thin surface or feature which is

Lamp Shade			revolved about an axis of revolution. Using the

Revolved Boss/Base this can be easily created.

What plane will the sketch be created on?

Sketch Lamp			Create a sketch on the front plane

Shade				using the dimension shown.

Note: The sketch for the lamp shade

is just a line.

Thin Revolve			Select Revolve Boss/Bass.

The following message will pop up.

The programme gives you the opportunity to close the sketch. If you select ‘Yes’ (to close the sketch) a fustrum of a cone (solid feature) will be created.

In this case you want the sketch left as a line so that a thin feature is created.

Select NO in the dialogue box.

Note: When using Revolve Boss/Base to model a part the sketch profile

must be closed (complete).

Enter Parameters		Thin Feature will now be automatically

be ticked. Enter thickness of 1mm.

Shade Supports		Select top surface of the lamp

pole as shown.

Note: Select the Normal To view.

Sketch supports		Create the sketch shown, using circle

and line commands.

Dimension the sketch as shown

Note: Use power trim to remove unwanted

lines in sketch.

Extrude Boss/Base		Extrude the sketch using the

Blind end condition and a

Depth of 6mm.

Display Style			Change the display style to

Hidden Line Visible

Note: This allows you to see through

the lamp shade to the support already

created.

Sketch Radial Support	Select the face surface as shown

Create rectangular sketch about the

the centerline as shown.

Smart Dimension as shown.

Extruded Boss/Base		Extrude the sketch using the Up

To Surface end condition.

Select the inner surface of the shade and

click correct direction        in the

FeatureManager window

Repeat Extrude		Repeat the procedure on other side of

centre piece for other arm.

Rename Features		Each of the features in the FeatureManager

should be renamed as shown. This allows each

feature / sketch to easily identified later if necessary.

Add Texture			Right hand click on the feature Stem,

select Textures.

Scroll down through the SolidWorks

Textures to Wood.

Select Pine inside the wood menu as

shown

Select OK

Add textures to 		Repeat the above procedure for each of these

other features			features

- Design Cut

- Base

- Bottom Fillets

- Hole in Stem

- Hole in Base

Note: As the lamp has been created as a part, and not

as an assembly, each individual feature will have to be

textured separately.

Add appearance		Right hand click on the feature Lamp

to lamp shade			Shade, select Appearance and Color.

Choose an appropriate colour from

the colour swatch.

Make lamp shade		Scroll down the Property Manager to Optical

Transparent			Properties.

Adjust the Transparency setting to 0.45

as shown. Select OK

Add Texture to		Add an appropriate Texture to

Radial Support		the radial support.

Lesson Complete!

Other Possible Revolved Cuts Options

Center Punch                             Nail Punch		                            Architrave Block

Table Leg			               Block                                                     Mallet

Where is the Revolved Cut feature used in the mallet?

The shaping on the handle is created using the revolved

cut feature as shown.

# Text boxes

End Point

End Point

Sketch Profile

Sketch (contour)

Axis of Revolution