### Introduction to Revolve -  A Glass

Object Analysis sheet

Prerequisite Knowledge	Previous knowledge of the following commands are required to complete this lesson, sketching (line construction, dimensioning, Text), Fillet, Extruded Boss/Base

Commands Used	This lesson includes Sketching (Centerline, line, Smart Dimension, Text, fillet),  Revolve Boss/Base, Fillet and Edit Materials.

Where to start?		If you wish the Glass to end up sitting

on the Top Plane (Horizontal Plane) as

shown.

.

Getting Started		In this case the Sketch will be setup

on the Front Plane, as the glass is in

the vertical position.

Select Sketch         on the features

command toolbar.

Select the Front Plane, the front plane

will move into the normal view, as shown.

Create the profile		Create the sketch using the line command

and dimensions shown.

Note: Sketch is not yet Fully defined.

Diameter

Dimensions	Some dimensions should be diameter dimensions in the finished revolve feature. For these dimensions, always select the centerline (axis of revolution) as one of the picks. You will then have your choice of either a radius or diameter dimension, depending on where you place the dimension text.

Note:	This option is only available if a centerline is used as the axis of the revolution.

Dimension between the centerline and the outer vertical

edge to create a horizontal dimension.

Do not click to place the dimension text just yet.

Notice the preview is a radius dimension.

Move the cursor to the right of the centerline.

The preview changes to a diameter dimension

as shown.

Click to place the dimension text. Change the 				value to 70mm.

Set bottom diameter to 60mm as shown.

Adding Fillet			Select Tools/Sketch Tools/Fillet or select  					Fillet    from the sketch toolbar.

Enter a Radius of 5 mm

Select inner lines of the sketch, as shown.

Creating the feature		Select Features from the Command Manager. The Features toolbar has now 				replaced the Sketch toolbar along the top of the screen

Choose Revolve Boss/Base   , the sketch rotates

to a trimetric view with a preview of the proposed

revolve.

Revolve Feature Settings	The PropertyManager

appears with these default

end conditions.

The Glass will default to a preview as shown.

Lets analyze the

Propertymanager

= Axis of Revolution

Axis of Revolution		In this case SolidWorks has recognized

the centerline as being the Axis of

Revolution. As the sketch was dimensioned

from the centerline to create the diameter

dimensions of the glass.

If different centerline was required it would be

selected from this area

Revolve Direction		Select          Reverse Direction. The Revolve will

now revolve to opposite direction as shown.

Revolve Type			Select Mid-Plane in Revolve Type window as shown.

Ene

The sketch (Profile) will now revolve

through 900 Mid-Plane as shown.

Note: Each of these options allow you to

Manipulate the Revolve feature to suit the part.

Selected Contours		Allows you to select individual sketches (Profiles)

which are to be revolved about an Axis.

Enter Required 		Enter              Angle = 3600.

Parameters

Select One-Direction			      in

Revolve Type window

Click OK button        to create the feature.

Completed feature		This is the first completed feature of the

part. The sketch has been absorbed into

the REVOLVE 1 feature in the Feature

Manager.

Rename Feature

Add Top Fillet		Select the Fillet option. The fillet options appear

in the property manager.

Set the Fillet Type to Full Round Fillet

Note: The top edge of the glass is semi-circular.

By choosing Full round fillet it is not necessary

to enter a radius and if the glass feature is edited,

This feature will not need to be edited.

Face Selection		Using Items To Fillet window, select the

appropriate face within window.

Select the faces of the glass in sequence.

Sequence of selection		Using the Features Manager selection windows select the

faces in the following sequence.

1. Select Inner face of Glass.

2. Select Top face of the Glass

3. Select Outer Face of the Glass

Add Bottom Fillets		Add 3mm fillets to the edges shown.

Rotate Glass in position 	Select Standard Views from view toolbar at

for bottom text		the top of the SolidWorks window as shown.

Select Bottom to rotate the Glass

into a bottom view as shown.

Text

Generating the Text		Create a sketch on the bottom surface of 						the glass.

Select Centerpoint Arc              command from the

sketch tool bar.

Select center point and construct semi-circle.

Note: Line guide sketch will obstruct the

Extrusion of the Text. The properties of the

line / semi-circle must be changed first to a construction line.

Change Properties		In order to change the properties of the semi-circle

to a construction line.

Select the semi-circle in the sketch.

For construction will be unchecked      in the

PropertiesManager.

Select this to change properties as shown

Dimension Arc		Radius = 10mm

Add Text			Add Text to sketch as shown.

Front = Arial Black

Units = 3.0 mm

Align = Center

Extrude Boss/Base the sketch to

a thickness of 1mm

Edit Materials		Right hand click on the part name, select

Edit Material.

Scroll down through the SolidWorks

Materials to Other Non-metals.

Select Other Non-metals and select

Glass as shown.

Select OK

Other Possible Revolve Options

# Text boxes

Features Manager

1

2

Axis of Revolution

Sketch (Contour)

3