### Introduction to Sweep - Shell Structure part (B)

Prerequisite Knowledge	Previous knowledge of the following commands is required to complete this lesson, sketching (line construction, dimensioning, parabola), Swept Boss / Base, Surface cut, Shell, apply appearance.

Focus of the Lesson	Sweep creates a base, cut, or surface by moving a profile (section) along a path.

On completion of this lesson you will have the used the following aspects:

- Swept a sketch profile along a path to create swept boss / base.

- Examined the keep normal constant option within the sweep feature.

- Surface cut to cut away unwanted elements of the model.

- Shell the structure to required shape.

- Applied a colour.

Commands Used	This lesson includes Sketching (line, Smart Dimension, parabola), Swept Boss / Base, Surface Cut, Shell and Appearance.

Where to start?		Initially you must consider the following:

What sketch is required for the Profile of the

shell structure?

What sketch is required for the Path of the

shell structure?

Profile  -   Parabola

Path    -   Parabola

Plane selection		On which planes should the sketches for

the Profile and Path be created?

The Profile will be created on the

right plane and the Path on the front

plane as shown.

Note: By using the default planes like this

it simplifies sketching the model.

Getting Started		Starting with the sketch for the profile of

the sweep.

Select Sketch          on the features

command toolbar.

Select the Right Plane, the right plane

will move into normal view, as shown.

Save part			Save        part as Shell Structure.

Sketch the Profile		Create a sketch of the axis using

the centerline command.

Note: The centerline is drawn from

the origin.

Parabola Command		Select Parabola              on the sketch toolbar.

OR

Select tools, sketch Entities and

Parabola.

Draw Parabola		When selected the pointer changes to

Click to place the focus of the parabola along

the axis.

Extend from the focus and select

the vertex of the parabola as

shown.

Place the parabola		Select the outline of the

parabola as shown.

He ends of the parabola cannot be placed easily at this stage, therefore the ends 			are drawn in any position and repositioned afterwards.

Click OK button        to create the parabola.

Add Relations		Select one endpoint of parabola.

Hold down the control key, choose

the origin and the other endpoint

of the parabola.

On the left hand side choose Horizontal

from the Add Relations dialog box shown over.

Construct Base		Construct base line as shown.

line

Dimension sketch		Dimension sketch as shown.

Note: The sketch is now fully

defined as it is now black.

Exit sketch and 		On completion of the sketch, confirm the sketch.

Rename

Rename the sketch as ‘Parabola Profile’

Sketch the Path		Create a sketch, on the front plane for the

Path.

Select normal-to                      to get the

below view of the model.

Create sketch			Select centerline                 and

create the sketch show.

Note: the centerline is drawn

from the top of the parabola.

Draw parabola		Select parabola and sketch the

axis and ordinate of the second parabola

as shown.

Fix end point of		Select the ‘Profile Parabola’ and the endpoint

the parabola			of the parabola (path) as shown.

The properties window offers a number of

choices. Choose pierce

Note: The ordinate of the parabola has been

repositioned as shown.

Add relation 			Select endpoint of axis line

and the vertex of the ‘Profile Parabola’.

Select merge                      in the

properties window.

Dimension parabola		Smart dimension the parabola

as shown.

Rename sketch

Swept Boss/Base		Select the parabola as the profile and semi-parabola as the path.

Note: The angle between the profile and the path is maintained as the profile is swept along the path.  This is the default condition.  Therefore the profile (Parabola Profile) is not maintained in a vertical position, as required in this case. This can be seen in the preview.

Edit orientation		In the FeatureManager of sweep. Select

options. Open the menu under

orientation/twist type:

Select keep normal constant. The preview

will now change as shown below.

Note: By using the keep normal constant option, the sweep section

remains parallel to the beginning parabola (profile) at all times.

Click OK button        to create the feature.

Create horizontal		As it is a horizontal cut the top plane

base				can be used as the cut surface.

Select the Top plane in the

FeatureManager.

Cut with surface

From the top toolbar, select insert,

cut, with surface.

SurfaceCut			The featureManager will appear with

the top plane selected as the surface cut

as shown.

The direction of the cut can be selected

using the flip cut           option.

The arrow in the middle of the part indicates

which side of the part is going to be removed

when cut.

Click OK button        to create the surface cut.

Shell out the part		Select shell              on the features toolbar.

Select the front surface, bottom surface and

the back surface of the part to shell.

Enter thickness of 1mm.

Change appearance		Right click on the part name,

select the beach ball and then the Shell

structure.

Add appropriate colour from the palette.

Lesson Complete!

Other Possible Sweep Options

2007 Higher Level					2003 Higher Level

2001 Higher Level					1999 Higher Level

# Text boxes

Vertex

Focus

Arrow