### CONTAINER EXERCISE

Prerequisite knowledge        To complete this model you should have experience of the following:

Sketching, Extrude Boss/Base, Fillet, renaming features and adding colour.

Focus of lesson  			This lesson will focus on using the following new feature commands

Draft, Shell, Rib.

Commands Used             	This lesson includes Sketching,Draft,Shell, Fillet and Rib.

Renaming features and adding colour

Save File                              	Select File, Save As, Filename “Container”

Getting Started	         		Create a sketch, on the top plane

using the dimensions shown.

Position the sketch such that the origin

is at the intersection of the diagonals.

Introducing Draft               Draft  is used when a sketch

is to be extruded at an angle.

Draft allows you to either extrude

the model angled outward or inward.

Where to find it?	         	Select Extrude Boss/Base	         from the features toolbar or

From the Insert menu, select  Boss/Base and Extrude. Draft is an

Option from the Extrude menu which appears on the left.

Using Draft                       	In the Extrude menu select a height of 100mm

and a draft angle of 8.00deg.  Activate the Draft

option, by pressing the Draft on/off icon       .

In this case we want an outward Draft so we

need to tick the box Draft Outward as shown.

Draft allows you to extrude every face

of the sketch at an angle, as shown.

Renaming a feature		Select the feature in the Feature Manager

Tree. Press F2.

The feature name will be

`highlighted with a flashing

cursor on the right hand side.

Type the new name “Container”

to replace it.

Introducing Shell                 Shell is always added to the solid rather than the sketch and is					           		hence referred to as an applied feature. It allows you to create a thin walled

model.

Where to find it                    Select the Shell tool           from the features toolbar or

from the Insert menu, select Features/Shell…

Apply Shell		         Select the Surface you wish to shell from, in this case we will select the

Top Face by left clicking on it. The Surface you

Select will be the open side of the container, this is why

We select the Top surface.

Having selected Shell, the Shell options

appear in the property manager.

Select 2.00mm as D1 (Wall thickness)

Face 1 Top Face is already selected

Click OK           to Shell the Container.

Rename Feature as before by

highlighting the feature and

pressing F2.

Fillet                                      Apply Fillet to the container, using:

Constant radius

3mm Radius

Select edges shown

In green

To Rotate the Container to view the edges to be filleted

Select            rotate view from the view toolbar and then by

holding down the left mouse button rotate the model.

Rename Feature as before by

highlighting the feature and

pressing F2.

Introducing Rib           	The Rib tool allows you to create Ribs using a minimal sketch.

In this case we will use rib to divide the container into two

compartments. Ribs need to be extended to a surface and so they usually

require a plane being offset from the model.

Where to find it?            Select the Rib tool          from the features manager or from the Insert menu,

go to Features and select Rib.

Apply Rib 			Begin as mentioned by setting up a plane offset from the base of the

Container.

Setting up a Plane        From the features toolbar select                and select                      or from

the Insert menu select Reference Geometry and select Plane.

Planes can be set up using many different methods

But in this case we will offset the plane from the

Base of the container by

Selecting the inside base of the container, (the base turns

Green and the plane appears as a yellow preview).

Setting the distance as 60mm

Click  OK        to place the plane in position.

Sketching the Rib        	Now that the plane has been set up we can draw a sketch of

the Rib on it. The Rib sketch can be simple or complex, and in this case it

is simply a line.

Before sketching it is important to make sure that we are sketching

on the Plane, so move the cursor over the plane and when it turns red

left click on it. The Plane will then turn green to show it is selected.

Sketch a line down the centre

of the plane using

the dimensions shown.

Applying Rib  	Select the Rib tool          from the features manager or from the Insert menu,

go to Features and select Rib

The Rib option appears on the manager

Tree on the left hand side. From this select the

Following

T1 = 1.50mm

Extrusion direction Vertical

Draft of 2.00deg by pressing the draft

On/off button

Select draft outward

Select OK

Hiding The Plane         	At this point the plane is still visible in the drawing and is not needed

as part of the finished drawing, so we can now hide the plane.

To do this right click on Plane 1

on the feature manager tree  and select

Hide

The Plane is no longer visible.

Add Colour to

the Container	From the feature manager,

Right click on Container and

Select “Appearance” and

“Colour”

From the colour pallet which

Appears on the left hand side

Select your choice of colour.

Alternate exercises

1.

2.