### Introduction to Loft -  Shampoo Bottle part (A)

Prerequisite Knowledge	Previous knowledge of the following commands is required to complete this lesson, sketching (line construction, circle, Arc, fillet, add relations, dimensioning), Inserting Planes, Revolve Boss/Base, Fillet.

Focus of the Lesson	Loft creates a solid feature by making transitions between profiles.

A loft can be a base, boss, cut, or surface. You create a loft using two or more profiles. Only the first, last, or first and last profiles can be points. All sketch entities, including guide curves and profiles, can be contained in a single 3D sketch.

On completion of this lesson you will have the used the following aspects:

- Inserted reference planes.

- Create a Lofted feature using guide curves.

- Revolved a sketch contour about an axis to create a Revolve Boss/Base.

Commands Used	This lesson includes Sketching (line, circle, arc, fillet, Smart Dimension), Inserting Planes, Loft Boss / Base, Revolve Boss/Base, Fillet and Appearance.

Where to start?		In analyzing the shampoo bottle, the

sketches required to form the bottle

must be first identified.

- What is the base sketch?

- What is the top sketch?

- What guide sketches are required?

Identifying the sketches	The base sketch will be lofted along the

guide curves up to the top sketch to

create the bottle feature.

Plane selection		On which planes should these sketches

be created?

The feature is create by lofting the base

sketch along the guide curves. Therefore

the guide curves (in this case) will have to

be setup on the midpoint of the base.

By setting up the base sketch centrally about

the origin. The front plane and right plane

can be used to sketch the guide curves.

Note: A plane will have to setup for the

top sketch.

Getting Started		Create the sketch using the rectangle

command on the top plane.

Centre the sketch on		Ensure that the rectangular sketch remains centered about

the origin			the origin.

Right click on one side of the rectangle and

choose Select Midpoint. Holding down the

control key choose the origin.

In the FeatureManager, choose Vertical/

Horizontal. Repeat procedure for other

Side.

Add dimension		Smart dimension the sketch as shown.

Add fillets			Add sketch fillets radius 5mm to

rectangle.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Base Sketch”

Save part			Save        part as Shampoo Bottle.

Insert Plane			Select Insert, Reference geometry and

plane.

Expand the part design tree by checking

the          plus sign in front of the part.

Choose the top plane as the reference entity and

set the distance as 160mm.

Click OK button              to create the plane.

Rename plane		Rename the plane a “bottle top”

Top sketch			Select sketch and create a sketch on the

bottle top plane as shown.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Top Sketch”

Sketch guide curves		Select sketch and create a sketch on the

front plane.

Select 3 Point Arc             , sketch an arc

as shown.

Select Centerpoint Arc              , sketch an

arc as shown.

Note: The centerpoint of the arc is aligned

with the top sketch. (use the inference geometry

to locate)

Add Relations to		Select Add relations                from the

the arcs			sketch toolbar.

Select the two arcs and choose Tangent

Click OK button              to add relation.

Add Relations between	Add relation to endpoint of the guide curve and

sketches			the top circle.

Select the endpoint and top circle. Choose Pierce

from the add relations window.

Note: Rotate the sketch to an isometric view to

get a clear view of the sketches.

Add relation to the endpoint of the guide curve

and the base.

Select the endpoint and base. Choose Pierce

from the add relations window.

Add dimensions		Add the centerlines and dimension

as shown.

Mirror Sketch		Select Mirror Entities             from the sketch

toolbar, mirror the guide curve to the opposite

side.

Select the guide curve as the entities to mirror

and select the centerline as the mirror about

axis.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Side guide curves”

Sketch front guide		Select sketch and create a sketch on the

curve				Right Plane.

Using line and 3 Point Arc create the sketch

shown.

Note: Select Normal To                          to

get a view perpendicular to the Right Plane.

Add Relations between	Add relations between the endpoints of the guide

sketches 			curve and the top circle / Base.

Select the endpoint and top circle. Choose Pierce

from the add relations window.

Repeat the procedure for the base.

Add Dimensions		Dimension the sketch as shown.

Add centerline		Construct a centerline from the origin

up to the top circle.

Note: To complete the mirror entities a centerline is required.

Mirror Sketch		Select Mirror Entities and mirror sketch.

Exit sketch and 		On completion of the sketch, Exit the sketch

Rename

Rename the sketch a “Front guide curves”

Creating the feature		Select Features from the Command Manager. The Features toolbar has now 				replaced the Sketch toolbar along the top of the screen

Choose Lofted Boss/Base

OR

From the top toolbar select Insert,

Boss/Base and Loft.

Loft Feature Settings	The PropertyManager appears as shown.

Note: The loft feature cannot recognize

which of sketches are profiles or guide curves.

Therefore all the selections are currently

empty.

Lets analyse the Propertymanager

Profiles selection		Profiles           - determines the profiles used to create the loft.

Select the Top sketch and Base sketch.

Note: Lofts are created based on the order of profile selection. In this case we are

using two profile sketches (the preview of this loft can be see above). If there are

more than two profile sketches this must be selected in the correct order.

Sketch Tools			At the bottom of the Loft Feature Setting there is

a window called Sketch Tools.

The sketch tool are most useful when defining the

loft sections and guide curves from contours within

the same sketch.

Select             - Select sketch entities only. Sketch contours are not selectable.

Chain Contour Select             - Select one sketch segment at a time as a contour. Switch to single contour selection to select the profiles and guide curves separately.

Single Contour Select           -Select chains of sketch segments as contours. The software selects the best chain of sketch segments. Sketch chaining prefers planar contours over non-planar contours, and closed contours over open contours

Guide Curves Selection	Guide Curves           - sets a path along which the profile will loft.

Select Single Contour Select           to select the guide curves.

Select the Guide Curves window and choose one of the guide curves as shown.

Note: The guide curves will not be selectable unless the single contour select

sketch tool is first selected.

Select the remaining 3 guide curves as shown.

Thin feature			Select thin feature by ticking the box in the top left corner as shown.

A window opens with a number of Options. Solidworks has entered

some default parameters which can be adjusted.

The preview of the Shampoo Bottle changes to a thin wall sweep as shown.

Deselect the thin feature.

Confirm Feature		Click OK button        to create the feature.

Rename feature		Rename the loft feature “Bottle”.

Revolve the Top		Create a sketch on the front plane.

Using the line and arc commands create

and dimension the sketch as shown.

Note: The sketch is created on the midpoint

of the bottle.

Revolve Boss/Base		Revolve the sketch using the 300 line as axis of revolution and sketch as

contour profile. Revolve angle of 3600.

Rename sketch and		Rename the revolve feature and sketch

feature			as shown.

Add bottom fillets 		Add 3mm fillets to the bottom edges

shown.

Add bottom fillets 		Add 1.5mm fillets to the top edges

shown.

Change appearance		Right click on the feature name (Bottle)

select appearance and colour.

Add appropriate colour.

Repeat the procedure for the Bottle Cap.

Lesson Complete!

# Text boxes

Guide Curves window

Endpoint of guide curve

Base Sketch

Guide Curves

Mirror About

Entities to Mirror

Guide curve is now intersecting the circle.

Guide curves positioned at the midpoint

Top Sketch

Tick Here