### Whistle Exercise

Object Analysis sheet

Commands used:	Sketch Circle, Line, Rectangle, Centre Arc, Trim, Add Relation, Mirror sketch, Smart dimension, Extruded Boss/Base, Cut Extrude, Revolved Boss/Boss, Fillet, Shell, & Edit Material

Approach to Lesson:

Create sketch for the body

of the whistle	Create the sketch on the Front Plane using the Circle and Line sketch commands.

Use Trim to remove arc and line.

Make this line and the Origin Coincident by using Add Relation

Use Smart Dimension to 				dimension the sketch

Whistle body			Extrude the sketch using Extruded Boss/Base

Select Mid Plane as the end condition and a distance of 18mm.

Rename the feature as ‘Whistle Body’.

First cut to

mouth of the whistle 	Create one half of the sketch on the top surface of the whistle using the Line command.  Sketch a Centreline and Mirror three lines about the centreline to create the other half. Smart Dimension the sketch.

Cut Extrude			Cut Extrude using this sketch.  Select Up to Next as the end condition.

Rename the feature as ‘First cut’

Second cut to

mouth of whistle	Create sketch on the top surface of the whistle using Centreline and  Centre Arc.

Make the arc tangential to the right hand 				edge by using Add Relation

Smart Dimension.

Cut Extrude	Cut Extrude using this sketch (line).  Through All is the automatic end condition.  Ensure the direction is pointing away from the body of the whistle

Rename the feature as ‘Second cut’.

Apply fillet to

top edges			Apply a 1mm fillet to the top 	edges of the

whistle.

Rename the feature as ‘Top fillet’

Raised area

for ring attachment	Create the sketch below on the Front Plane using Line, Add Relation and Smart Dimension.

Revolved Boss/Base to

raised area 			Use Revolved Boss/Base 				to create the area.

Rename the feature as ‘Raised area’.

Shell				Shell the whistle with a wall 					thickness of .5mm.  Remove one 				face.

Rename the feature as ‘Shelling of 	whistle’.

Opening	Create sketch on the top surface of the whistle using a Rectangle

Smart Dimension

Extrude Cut with this sketch to create the opening. Select Up to Surface as the end condition and select the inside surface.

Rename the feature as ‘Opening’.

Hole				Create the sketch on the front 				plane

Extrude Cut with this sketch to create the hole. Select Mid Plane as the end condition and a distance of 10m

Rename as ‘Hole’.

Edit Material			Apply a Chrome Stainless Steel finish

In the features manager tree right click on the whistle

Select appearance and then select edit material as shown.

Select Chrome stainless steel as the material and apply.

Choose OK

Add in notes on the properties of the whistle when the material is applied. Note the difference between appearance and material